## Slide 1
Integrated Enterprise Network | 1
Integrated Enterprise Network Using Cisco Packet Tracer
CCNA Networking and Cybersecurity Project
Mohammad Umar Naeemullah Shaikh
Cyber Security & Ethical Hacking with AI
IT-Vedant (Dadar) | Academic Year 2026
Guide: Kadir Ail

## Slide 2
Self Introduction
Integrated Enterprise Network | 2
Mohammad Umar Naeemullah Shaikh
Course: Cyber Security & Ethical Hacking with AI
Institute: IT-Vedant (Dadar)
Guide: Kadir Ail
"Hello everyone, my name is Mohammad Umar Naeemullah Shaikh. I am studying Cyber Security & Ethical Hacking with AI at IT-Vedant, Dadar. In this project I built and documented an enterprise network in Cisco Packet Tracer to understand routing, network services and security."
Cisco Networking
Network Security
Cybersecurity
Ethical Hacking
Linux
Python
Troubleshooting
Notes: Introduce yourself: name, course at IT-Vedant, and that this project is where you applied networking and security. Keep it to about twenty seconds.

## Slide 3
How This Project Will Support Industries
Integrated Enterprise Network | 3
IT Companies
Banking
Education
Hospitals
Corporate Offices
Retail
Government
Multi-branch Firms
Project concept | Industry benefit
Hierarchical Main–Core–Site design | Scales by adding sites without re-addressing
OSPF multi-area + eBGP | Fast, stable routing between locations
DHCP on site routers, central DNS/web | Automatic addressing; shared services
ACLs, SSH v2, NAT/PAT, STP | Controlled traffic and secure management
Packet Tracer is a simulation: these are representative enterprise practices, not a production deployment.
Notes: Any organization with several sites needs this: banks with branches, hospitals, colleges, retail chains. My project shows the same building blocks. Remember it is a simulation.

## Slide 4
Challenges Faced During the Project
Integrated Enterprise Network | 4
Supplied file had cabling only: all interfaces down, no IPs, services off
Planning VLSM: /30 links and /28 LANs without overlap
Matching brief, screenshot and .pkt (16 vs 17 routers, ATM site)
13 per-site servers not cabled
Serial DCE/DTE and clock rate setup
Multi-area OSPF and ABR design
eBGP: avoiding loop rejection between Head Office routers
NAT/PAT and ACLs without blocking OSPF, BGP or SSH
DHCP exclusions for printers, servers, switches
Keeping addressing, CLI and documentation consistent
Notes: These are the real issues in this project: the file had no configuration, the counts did not match, and every table had to stay consistent with one addressing plan.

## Slide 5
How I Resolved the Issues
Integrated Enterprise Network | 5
Issue | Analysis | Solution
Count mismatch | Compared brief, screenshot and .pkt | Baseline 17 routers / 27 switches; extras recorded as verification issues V1–V10
IP complexity | 156 PCs, 28 laptops, 14 printers, 16 servers | One VLSM plan: /30 from 100.1.0.0/24, /28 per switch segment
Routing design | Tree topology, many routers | Multi-area OSPF (areas 0–3), manual router IDs, passive LAN ports
BGP loops | Shared AS would reject routes | Core-R1 AS 65001; HO-R1..4 use AS 65101–65104
ACL / NAT impact | Management and routing traffic | Permit 100.x.x.x; NAT only for HO to server LAN
SSH / DHCP | Prerequisites and exclusions | Hostname, domain, RSA, VTY; excluded gateway, SVI, static hosts
Notes: For each issue I analysed first, then fixed it in the design. The key fixes were the single addressing plan, separate BGP AS numbers for each Head Office router, and recording every mismatch instead of hiding it.

## Slide 6
Project at a Glance
Integrated Enterprise Network | 6
17
Routers (2811)
27
Switches (2960)
156
PCs
28
Laptops
14
Printers
16
Servers
Sites: Main, 3 Core, Head Office, Branch, School, College
Routing: multi-area OSPF + eBGP; Services: DHCP, DNS, HTTP/HTTPS, NAT/PAT
Security: ACLs, SSH v2, secret passwords, STP protections

## Slide 7
Problem Statement and Objectives
Integrated Enterprise Network | 7
Problem
Supplied project had cabling only. A complete, consistent addressing, routing, services and security design was needed.
Document topology without altering it
VLSM plan: /30 links, /28 LANs
OSPF multi-area and eBGP
DHCP, DNS, HTTP/HTTPS for all sites
NAT/PAT at Head Office; ACLs at HO, BO, College
SSH v2 and hardening on all devices

## Slide 8
Complete Network Topology
Integrated Enterprise Network | 8
Author's Packet Tracer screenshot. Green = Head Office, cyan = College, orange = Branch Office, yellow = School.

## Slide 9
Network Architecture
Integrated Enterprise Network | 9
MAIN - R (100.0.0.0/24 server LAN: DNS, web, backup)
CORE-R1 · CORE-R2 · CORE-R3 (OSPF ABRs; Core-R1 = eBGP hub)
Head Office
HO-R1..4
Branch Office
BO-R1..3
School
SHC-R1..3
College
COL-R1..3
Each site router: Fa0/0 and Fa0/1 → two switches → PCs, laptops, printers
Tree topology: no redundant router path and no switch-to-switch link.

## Slide 10
Topology Verification Issues
Integrated Enterprise Network | 10
ID | Finding | Handling
V1 | Brief: 16 routers; logical list = 17; .pkt file = 19 | Baseline = 17
V2 | ATM-R1/R2, Switch18–21, Server8/17 only in .pkt | Excluded from baseline
V3 | Switches: brief 27, .pkt 31 | Baseline = 27
V4 | Servers: only 3 cabled (Main); 13 not cabled | 16 documented, 13 proposed
V5 | PCs: brief 154, names total 156 | 156 documented
V6 | COL-PC29 uncabled in .pkt | Assumed on Switch17 Fa0/6

## Slide 11
Device Inventory
Integrated Enterprise Network | 11
Site | Routers | Switches | PCs | Laptops | Printers | Servers
Main | 1 | 1 | 0 | 0 | 0 | 3
Core | 3 | 0 | 0 | 0 | 0 | 0
Head Office | 4 | 8 | 48 | 16 | 8 | 4
Branch Office | 3 | 6 | 36 | 12 | 6 | 3
School | 3 | 6 | 42 | 0 | 0 | 3
College | 3 | 6 | 30 | 0 | 0 | 3
Total | 17 | 27 | 156 | 28 | 14 | 16

## Slide 12
IP Addressing Scheme
Integrated Enterprise Network | 12
Block | Prefix | Used for
Main | 100.0.0.0/24 | Server LAN (gateway 100.0.0.1)
Core / WAN | 100.1.0.0/24 | 16 serial /30 links (.0–.63)
Head Office | 10.1.0.0/24 | 8 LANs (/28)
Branch Office | 10.2.0.0/24 | 6 LANs (/28)
School | 10.3.0.0/24 | 6 LANs (/28)
College | 10.4.0.0/24 | 6 LANs (/28)
/30: first IP = upstream (DCE), second = downstream
/28: .1 router, .2 switch SVI, hosts from .3
Hosts: DHCP; printers/servers static

## Slide 13
Router-to-Router Serial Links (/30)
Integrated Enterprise Network | 13
Link (DCE → DTE) | Interfaces | Subnets from 100.1.0.0
Main → Core-R1 | S1/0 → S1/0 | .0/30
Main → Core-R2 / Core-R3 | S1/1, S1/2 → S1/0 | .24/30, .28/30
Core-R1 → HO-R1..R4 | S1/1..S1/4 → S1/0 | .4, .8, .12, .16 /30
Core-R1 → BO-R1 | S1/5 → S1/0 | .20/30
Core-R2 → BO-R2, BO-R3 | S1/1, S1/2 → S1/0 | .32, .36 /30
Core-R2 → SHC-R1..R3 | S1/3..S1/5 → S1/0 | .40, .44, .48 /30
Core-R3 → COL-R1..R3 | S1/1..S1/3 → S1/0 | .52, .56, .60 /30
16 links in total. Example: Main S1/0 = 100.1.0.1, Core-R1 S1/0 = 100.1.0.2 .

## Slide 14
Router-to-Switch FastEthernet and LAN Subnets
Integrated Enterprise Network | 14
Site | Switches | LAN subnets (/28) | Gateways
Head Office | Switch 1-8 | 10.1.0.0 – 10.1.0.112 | 10.1.0.1, .17, .33 … .113
Branch | Switch 1-6 | 10.2.0.0 – 10.2.0.80 | 10.2.0.1, .17 … .81
School | Switch 1-6 | 10.3.0.0 – 10.3.0.80 | 10.3.0.1, .17 … .81
College | Switch 1-6 | 10.4.0.0 – 10.4.0.80 | 10.4.0.1, .17 … .81
Main | Switch 1 | 100.0.0.0/24 | 100.0.0.1
Fa0/0 → switch A, Fa0/1 → switch B (uplink on switch Fa0/1). Core routers have no LAN interfaces.

## Slide 15
OSPF Design
Integrated Enterprise Network | 15
IDs: Main 1.1.1.1, Core 2.2.2.x, HO 3.3.3.x, BO 4.4.4.x, SHC 5.5.5.x, COL 6.6.6.x
Process ID 1, manual router IDs
Area 0: Main LAN + Main–Core links
Area 1: Core-R1 domain; Area 2: Core-R2; Area 3: Core-R3
ABRs: Core-R1, R2, R3
Cost 50 on serials; LAN ports passive
16 adjacencies expected (FULL, point-to-point)
router ospf 1
router-id 2.2.2.1 ! CORE-R1
network 100.1.0.0 0.0.0.3 area 0
network 100.1.0.4 0.0.0.3 area 1
passive-interface FastEthernet0/0
interface Serial1/1
ip ospf cost 50
show ip ospf neighbor

## Slide 16
BGP Design
Integrated Enterprise Network | 16
Router | AS | Neighbor | Advertises
CORE-R1 | 65001 | 100.1.0.5, .9, .13, .17 | Re-advertises learned routes
HO-R1 | 65101 | 100.1.0.5 | 10.1.0.0/28, 10.1.0.16/28
HO-R2 | 65102 | 100.1.0.9 | 10.1.0.32/28, 10.1.0.48/28
HO-R3 | 65103 | 100.1.0.13 | 10.1.0.64/28, 10.1.0.80/28
HO-R4 | 65104 | 100.1.0.17 | 10.1.0.96/28, 10.1.0.112/28
Different AS per HO router lets Core-R1 pass routes between them
eBGP (AD 20) beats OSPF (AD 110) for Head Office prefixes
No redistribution; other sites learn via OSPF
show ip bgp | show ip bgp summary

## Slide 17
DHCP
Integrated Enterprise Network | 17
Discover
►
Offer
►
Request
►
Acknowledge
Each site router is the DHCP server
28 pools: <router>-LAN-A / LAN-B
Gateway = .1, DNS = 100.0.0.2, lease 7 days
Excluded: router, switch SVI, printers, servers
ip dhcp excluded-address 10.1.0.1 10.1.0.2
ip dhcp excluded-address 10.1.0.11 10.1.0.12
ip dhcp pool HO-R1-LAN-A
network 10.1.0.0 255.255.255.240
default-router 10.1.0.1
dns-server 100.0.0.2
lease 7
show ip dhcp binding

## Slide 18
NAT and PAT (Head Office)
Integrated Enterprise Network | 18
ip access-list extended NAT-TRAFFIC
permit ip 10.1.0.0 0.0.0.255 100.0.0.0 0.0.0.255
interface FastEthernet0/0
ip nat inside
interface FastEthernet0/1
ip nat inside
interface Serial1/0
ip nat outside
ip nat inside source list NAT-TRAFFIC
interface Serial1/0 overload
Router | Outside IP
HO-R1 | 100.1.0.6
HO-R2 | 100.1.0.10
HO-R3 | 100.1.0.14
HO-R4 | 100.1.0.18
Inside local: real host IP; inside global: router serial IP
Only traffic to the server LAN is translated

## Slide 19
Access Control Lists
Integrated Enterprise Network | 19
ACL | Where | Rule | Purpose
10 (std) | VTY, HO/BO/COL | Own site /24 + 100.0.0.0/24 | SSH from own site and servers
HO-IN | HO-R1..4 S1/0 in | Deny School and College to HO | Protect Head Office
BO-IN | BO-R1..3 S1/0 in | Deny School to Branch | Isolate untrusted School
COL-IN | COL-R1..3 S1/0 in | Deny School to College | Isolate untrusted School
NAT-TRAFFIC | Used by NAT | HO to 100.0.0.0/24 | Select traffic to translate
Each ends with permit ip any any (except the VTY list). OSPF, BGP and SSH use 100.x addresses and are permitted.

## Slide 20
SSH Secure Management
Integrated Enterprise Network | 20
All 17 routers and 27 switches
Hostname + domain project.local
RSA 1024-bit key, SSH version 2
VTY: SSH only, local login
VTY ACL 10 restricts source networks
Telnet refused
hostname HO-R1
ip domain-name project.local
username admin privilege 15 secret <password>
crypto key generate rsa general-keys modulus 1024
ip ssh version 2
line vty 0 4
transport input ssh
login local
access-class 10 in
show ip ssh

## Slide 21
DNS, HTTP and HTTPS
Integrated Enterprise Network | 21
Client
►
DNS 100.0.0.2
►
IP address
►
Web server 100.0.0.3
Name | Address
dns.project.local | 100.0.0.2
www / school / college .project.local | 100.0.0.3
backup.project.local | 100.0.0.4
Domain: project.local
DHCP gives clients the DNS server
HTTP (port 80) clear text; HTTPS (443) encrypted
Test: nslookup www.project.local, then http:// and https://

## Slide 22
Security Architecture
Integrated Enterprise Network | 22
ACL
SSH v2
HTTPS
NAT / PAT
STP
Secret passwords
Layered: Layer 2 (STP), Layer 3 (ACL, NAT), management (SSH, banners, VTY), application (HTTPS)
Lab passwords and RSA 1024 are not production-grade

## Slide 23
Testing and Verification
Integrated Enterprise Network | 23
Area | Commands | Result
Basics | show ip interface brief, show ip route, ping, traceroute | Verified
OSPF | show ip ospf neighbor, show ip protocols | Verified
BGP | show ip bgp, show ip bgp summary | Verified
NAT / DHCP | show ip nat translations, show ip dhcp binding | Verified
ACL / SSH | show access-lists, show ip ssh | Verified
DNS / Web | nslookup www.project.local, browser http/https | Verified
The report states actual results stay "To be verified" until the configuration is run in Packet Tracer.

## Slide 24
Advantages and Limitations
Integrated Enterprise Network | 24
Advantages
Easy to extend hierarchy
Multi-area OSPF keeps updates local
VLSM wastes no space
Central DNS/web; router DHCP
Layered security
Limitations
No redundancy (tree)
Only 3 servers cabled
No VLANs
NAT/BGP mainly demonstrative
Results not yet captured

## Slide 25
Future Scope
Integrated Enterprise Network | 25
Redundant core links
VLANs + port security
Firewall / ZBF
AAA RADIUS/TACACS+
Syslog + NTP
IPv6
HSRP / VRRP
QoS
Cable per-site servers
ATM site
GNS3 / EVE-NG

## Slide 26
Integrated Enterprise Network | 26
Conclusion
Documented the Packet Tracer topology exactly as cabled
One addressing plan drives routing, services and security
Mismatches recorded, not hidden
Next step: apply the configuration and capture test results
Thank You